## Slide 1
Radio Frequency Readout Device (RFRD)
May 1718 RFRD

## Slide 2
Brandon Baxter – Leader, IC Team
Vaughn Dorsey –Webmaster, Reader Team
Luke Myers –Communication Leader, IC Team
Kurt Turner –Key Concept Holder, IC Team
Aaron Haywood – Antenna Team
Robert Buckley – Reader Team
Mehdy Faik – Antenna Team
Kellen Yoder – Reader Team
Michael Miller – IC Team
Team Members Clients
Primary Advisor/Client:
Dr. Qiao
Secondary Advisor:
Dr. Song
Notes: Slide 2:
Everyone?

## Slide 3
Purpose / Background
Multi-purpose Remote Readout Device
Specific Test Scenario: Street lamps across the U.S.
Each lamp
  6 – 8 bolts
  Thousands of lamps per state
Problem
  Bolts become loose over time
  There is a need for a method of detection of these loosened bolts
Notes: Slide 3:
Brandon –
We have been tasked with creating an RFID-like system that can measure capacitance at a distance. The purpose of this system is due to

## Slide 4
Specifications
Requirements
  RF technology & Energy Siphoning  Create RF tag
  Value changing readout RF device
  RF tag Specs
    Measure Washer Separation via Capacitance
    Report Capacitance to Reader
  Important Constraints
    Power (Passive Tag)
    Range (5 meter distance)
    Cost (< $0.50 per Tag)
Notes: Slide 4:
Luke -

## Slide 5
Research
Findings
  5 meter range  Suggests we neeed to use 900 MHz RF technology
    Source 1: http://ieeexplore.ieee.org/document/6934233/
    Source 2: http://ieeexplore.ieee.org/document/4396783/
  Need a low power capacitance sensor
  Need a state machine capable of changing output of a section of machine based on sensor data
Notes: Slide 5:
Robert -

## Slide 6
Project Roadblocks
Reader Team
  900 MHz Technology
    Cost prohibitive
    Difficult to determine if high cost equipment implementation will be successful
Antenna Team
  900 MHz outside our ability to test
  Some simulation possible, but access to this equipment is not available to test properly
IC Team
  Difficult to create designs with unknown available power details
Notes: Slide 6:
Reader (Robert/Kellen/Vaughn) -
Antenna (Mehdy) –
IC (Kurt) -

## Slide 7
New Approach
900 MHz  13.56 MHz for Design
Reader Team
  Design our own reader
    More cost effective in early stages of design
    Allow for switching back to 900 MHz to involve a simple parts switch
Antenna Team
  13.56 MHz is a possible frequency for us to test with equipment available
IC Team
  Initial data from Antenna Team detailing amount of power we have  Started on a CMOS design
Notes: Slide 7:
Brandon – Talk about Frequency switch
Reader

## Slide 8
High Level of Entire System

## Slide 9
Current State: Antenna Team
Square Coil Antenna at 13.56 MHz
  Optimal performance in breadboard tests
  Logistics  Easier to implement
  Design Variables
    Trace Width & Thickness
    Number of Segments
    Footprint Size
    Orientation
    Presence of Dielectric
Notes: Slide 8:
Mehdy -

## Slide 10
Current State: Antenna Team
Notes: Slide 8:
Mehdy/Aaron -

## Slide 11
Current State: Antenna Team
Gain Plot
  Accounts for efficiency  Assumes source impedance match
  Optimal Gain for φ = 270°
  Power Received vs. Distance
    100 mW Transmitted  Friis Transmission Equation
R (m) | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5
Pr (mW) | 44.70 | 28.61 | 19.86 | 14.59 | 11.17 | 8.829 | 7.151
Notes: Slide 8:
Mehdy -
Question that may arise: What is the min and max power that is involved?

## Slide 12
Current State: Reader Team
Parts have arrived  Reader design has begun
Issues with initial design have been found.
  Oscillator does not work
  Power Output to Antenna is too low.
Notes: Slide 9:
Robert/Kellen – We recently ordered parts to create our first test version of our reader. We obtained parts two days before break, and found when we returned that our current design does not send enough power to the antenna. This has caused the range from tests to be very low, and we have not been able to receive a response from our test RFID tag. We are looking into different voltage controlled oscillators to improve the power to the antenna, and amplifiers if we cannot get enough from the oscillator.

## Slide 13
Current State: IC Team
Logic Circuit
Component Experimentation
Notes: Slide 10:
Michael -

## Slide 14: Current State: IC Team Prototype
Discrete Component Prototyping
Problems with high frequency noise

## Slide 15
Current State: Capacitance Sensor
Capacitance sensor is working in simulations
Transition Graph
  Discharge to reset
  Charge to sensor value
Notes: Slide 11:
Kurt -

## Slide 16
Current State: Loose/Tight
Pre tightened
Torqued to spec
Loosened over time
  Dielectric in base material
Notes: Slide 12:
Brandon/Luke –
Vaughn – App Design

## Slide 17
Looking Forward
Order more parts for improvements on working prototype
Improve simulation models for both IC and Antenna Teams
Redesigning current reader  Test
Eventually move design of Reader a PCB
Development of user interface app design
Notes: Slide 12:
Brandon/Luke –
Vaughn – App Design

## Slide 18
Questions?

## Slide 19
Logic Circuit Design

## Slide 20: Control Signals Design

## Slide 21: Sensor Testing
Simulating capacitor charging/discharging